## Slide 1: Visual Observer Training
Officer Brandon Karr
City of Pearland, Texas

## Slide 2: Visual Observer Definition
A person or persons who’s sole responsibility during a flight operation is to maintain visual line of sight (VLOS) of the sUAS to assist in the safe and legal operation of flight.

## Slide 3: Visual Observer’s Role
After take off, keep a direct line of sight with the UAS
Work with the pilot to ensure a safe flight
Keep open communication with the pilot
Identify and mitigate any unsafe conditions
Keep the pilot informed of any obstacles:
  Light poles
  Wires
  Trees
  Airplanes / helicopter
  Any other objects in the flight path
  People
  Birds

## Slide 4: VO Quiz
A person whose sole task is watching the sUAS to report hazards to the rest of the crew is called
  Visual observer
  Remote-PIC
  Person manipulating the controls
Who is ultimately responsible for preventing a hazardous situation before an accident occurs?
  The visual observer (VO)
  The Remote Pilot in Command (Remote PIC)
  The person manipulating the controls

## Slide 5
Near miss with helicopter
Birds and Drones
Drone vs Plane

## Slide 6: Scanning for Aircraft/Hazards

## Slide 7: Visual Observer Communication
Information needed:
Immediate action
  Planes/Helicopters
  Unprotected Persons
  Birds
Caution
  Approaching Obstacle
  Losing Line of Sight
    Next Visual Observer notification of acquiring line of sight.

## Slide 8: VO Communication
Hazard location in relation to the drone
  East of the drone, North of the drone, Ect.
VO’s suggested action to avoid collision or violation
  Climb, descend, maneuver east, terminate

## Slide 9: VO Quiz
The common procedure for scanning for hazards of flight is to:
  Scan the air from left to right, quickly multiple times.
  Scan the air from right to left in a circular pattern,
  Scan the air from center to left, then center to right in sectors, checking each sector carefully
The Visual Observer may use binoculars to assist in the ability to maintain visual line of sight.
  True
  False

## Slide 10
Night sUAS Operations

## Slide 11: The Human Eye

## Slide 12: The Human Eye
As light enters the eye it passes through the lens and strikes the retina. The retina contains millions of Rods and Cones.
  Rods
    Outnumber Cones 17:1
    Used for low light image processing as well as peripheral vision.
  Cones
    We use cones to see motion, detail, and color.
    Cones require a high level of illumination to function.
    Decrease in density from the center of the eye to the edge of the retina.
    The fovea is completely covered in only cones.

## Slide 13: VO Quiz
The Cones in your eye are used for:
  Detail
  Peripheral images
  Low light images
The Rods in your eye are used for:
  Low light image processing
  Detail
  Color

## Slide 14: Factors that Affect Night Vision
Night Vision Processing
Two blind spots
Lack of color vision
Reduced acuity
Reduced depth perception
Night myopia
Visual hypoxia
Night blindness
Effects of aging
Carbon monoxide, alcohol, drugs, fatigue, smoking

## Slide 15: Night Vision Processing
Process requires about 30 min
Rods become adjusted to darkness
Off-center viewing important during night flights
Smoking, carbon monoxide, hypoxia, certain drugs adversely affect night vision
Avoid bright lights to preserve night vision
Red light preserves night vision but severely distorts colors

## Slide 16: Two Blind Spots
Physiological blind spot
  Occurs due to the Optic nerve bundle entering the eye called the Optic Disk
    Not observed due to the other eye compensating.
Central blind Spot
  Due to there not being any rods in the Fovea
    Look approximately 15 degrees off to see detail.

## Slide 17: VO Quiz
The two blind spots in the eye are due to the optic nerve and the lack of rods in the fovea
  True
  False
Red light preserves night vision
  True
  False

## Slide 18: Lack of Color Vision
Due to the lack of light, rods cannot function properly. Thus, the ability to see color is decreased

## Slide 19: Reduced Acuity
Central vision blindness at night
High rod-to-optic nerve fiber ratio reduces acuity
  Again due to the ability to process light

## Slide 20: Night Myopia
Near sightedness occurs during dark focus
Periodically change focus distance

## Slide 21: VO Quiz
At night your ability to see color is:
  Increased
  Decreased
  Neither
Night Myopia is the night effect on the eye that causes near sightedness.
  True
  False

## Slide 22: Visual Hypoxia
The retina of the eye is more sensitive to hypoxia than any part of our body
One of the first symptoms of hypoxia is a decrease in night vision
Effects most noticeable starting at 5000’ above ground level to which you are acclimated
Smokers are much more susceptible to hypoxia due to the build-up of carbon monoxide in their blood

## Slide 23: Night Blindness
Functionally blind due to pigment deficiency in rods
Night blindness induced within 60 days on diet lacking vitamin A

## Slide 24: Effects of Aging
Pupil size decreases
Range of eye focus is reduced
Visual acuity is reduced
Color discrimination becomes more difficult
It takes longer to process visual information in general
Sensitivity to glare increases
Takes longer to read under dim light conditions

## Slide 25: Night Illusions & Limitations
Illusions
  Autokinesis (objects appear to shift)
  False reference (stars or lights near horizon)
  Venus and sirius (false aircraft)
  Night myopia (dilation, inability to focus)
  Somatogravic (acceleration with pitch)
Limitations
  Night blind spot (rods & cones, stars, etc)
  Light to dark adaptation (30min)

## Slide 26: Focused Scan Problems at Night
Night blind spot
  center portion of eye is blind at night
Night Scan
  look 10-150 away from what you try to see
  night vision is affected by altitude
  drugs, alcohol, smoking and fatigue adversely affect night and day vision

## Slide 27: VO Quiz
The night illusion autokinesis is when objects appear to shift when the observer stares directly at the object.
  True
  False
The night illusion False Reference is when the observer cannot discern where the horizon is located due to ground lighting creating the illusion to be stars.
  True
  False

## Slide 28: End
Questions, Comments, Concerns
281 825 2060
bkarr@pearlandtx.gov